## Slide 2: Week 3
Make sure everyone can stream sensor data over serial and that the values look correct
  Gyrosocpe (rotation)
  Accelerometer (direction of gravity)
  https://os.mbed.com/users/andrewbates11/code/pdiot-MPU9250-test/
Bluetooth example:
  sending multiple values
    https://os.mbed.com/users/andrewbates11/code/pdiot-ble-notify-array/
    Use NRF Connect app on Android phone
Task for this week:
  Collect test sensor data to be used for steptracking
  Combination of Button, MPU9250 test and BatteryService
  Note: Latet Mbed-os library won’t compile with the BLE examples. Roll back to version 5.5.7