## Slide 1: PDIOT Week 4
Last week: Sending Gyro and Accelerometer data over BLE
Android app
  Discover NRF board and notify sensor data using BLE
  Unpack sensor data
  Log to a CSV file for inclusion in the PDIOT step tracking dataset
Tools/libraries
  Android Studio is available on the Dice machines
    Type androidstudio3 from terminal
  Rxandroidble is a BLE library that saves a lot of time!
  If android version >= 6, you need to grant location/storage permissions in settings/apps

## Slide 2: Packing sensor data into byte array
The sensor sends a signed 16 bit integer (int16_t)
The Bluetooth library only accepts an array of 8 bit unsigned integers (uint8_t [])
You need to convert the sensor value for each axis into 2 8 bit values by splitting the 16 bit value.
  Int16_t sensor;
  b1 = sensor & 0xff;
  b2 = sensor >> 8;

## Slide 3: And recombine on the Android side
private float combineAccelerationBytes(Byte upper, Byte lower) { short unsigned_lower = (short) (lower & 0xFF); short value = (short) ((upper << 8) | unsigned_lower); return (value) / 16384.0f; }

## Slide 4: Steptracking dataset format
Store sensor data as a CSV file with the following format:
Start with dataset description lines
  #num_steps=n
  #num_upsteps=n
  #num_downsteps=n
  #sensor_position={upper_leg, lower_leg, hips, upper_arm, lower_arm}
  #sensor_side={left,right}
  #gait_type={walking, running}
  #surface_type{carpet, hard, smooth, uneven}
  #sample_rate=nnHz
Header row
  accel_x, accel_y, accel_z,gyro_x,gyro_y,gyro_z
Data: 1 sample per line. Acceleration in g, Rotation in degrees per second